## Slide 1: CPEN 211: Introduction to Microcomputers Lab 5 Introduction
Prof. Tor Aamodt
Notes: 1

## Slide 2
Consider the following line of “C” code:
f = (g + h) – (i + j);
Question: How does a computer take this line and actually compute “f” given values for “g”, “h”, “i”, and “j” using digital logic?

## Slide 3: Example (Lab 5)
Convert this program (in C or Java) into ARM:
f = (g + h) – (i + j);
Solution:
ADD t0, g, h // t0 contains g + h
ADD t1, i, j // t1 contains i + j
SUB f, t0, t1 // f gets t0 – t1,
// which is (g + h) – (i + j)

## Slide 4: Suppose: g = 5, h = 7, i = 10, j = 2
How might the computer remember these values?

## Slide 5: Register with Load Enable
5
1
5
0
5
1
5
7
5
7
0

## Slide 6: Register File

## Slide 7: Register File
Contains eight 16-bit registers
To read a register:
Put the register number on the readnum control signal (3 bits)
The value in the selected register will be driven on the output bus
(not aligned to the clock at all)

## Slide 8: Register File
Writing to the register file:
- Put the data you want to write on the input bus
- Put the register number on the writenum control signals (3 bits)
- When the clock goes high, the data is written

## Slide 9: Register File
Writing to the register file:
- Put the data you want to write on the input bus
- Put the register number on the writenum control signals (3 bits)
- When the clock goes high, the data is written

## Slide 10: Register File
Writing to the register file:
- Put the data you want to write on the input bus
- Put the register number on the writenum control signals (3 bits)
- When the clock goes high, the data is written

## Slide 11: Register File
Writing to the register file:
- Put the data you want to write on the input bus
- Put the register number on the writenum control signals (3 bits)
- When the clock goes high, the data is written

## Slide 12: Register File: Writing 5 into R0
16’d5
3’b000
1’b1
5
Writing a value into the register file is clock edge sensitive!

## Slide 13: Register File: Writing 7 into R1
16’d7
3’b001
1’b1
5
7

## Slide 14: Register File: Reading R0
3’b000
8’b00000001
5
7
5
Reading a value out of register file is purely combinational – no clock!

## Slide 15: Why only 8 Registers?
Smaller is faster
Reason: delay increases with length of wires
(Generally, all others things being equal, prefer computers to be faster.)
For arithmetic instructions in the Simple RISC Machine ISA all “operands” must be in the register file.
Other ISAs do not make same choice (x86).

## Slide 16: Example w/ Registers
The variables f, g, h, i, and j are assigned to the registers r0, r1, r2, r3, and r4, respectively. What is the compiled ARM code for the following C?
f = (g + h) – (i + j);
Solution:
ADD R5,R1,R2 // register R5 contains g + h
ADD R6,R3,R4 // register R6 contains i + j
SUB R0,R5,R6 // R4 gets R5 – R6,
// which is (g + h) – (i + j)

## Slide 17: Simple RISC Machine Datapath

## Slide 18: Datapath Control Inputs

## Slide 19
Each instruction takes between 1 and 4 cycles to execute: Each cycle, certain control signals are asserted to perform the required operations
Which control signals are asserted depends on which instruction is being executed. A decoder and state machine drives the signals at the right time. You’ll design that part in Lab 6.

## Slide 20
Multiplexers: Purely combinational logic: you could design these blocks with your eyes closed.

## Slide 21
Arithmetic Logic Unit (ALU): Does the actual computing. E.g., adding, subtracting numbers and performing logical operations (AND, NOT, etc…)
ALUop | Operation
00 | Ain + Bin
01 | Ain - Bin
10 | Ain & Bin
11 | ~ Bin
1 if result of ALU
operation is 0
and 0 otherwise

## Slide 22
Shifter unit: Useful to multiply one ALU
operand by 2 (or divide by 2). We can do
this by shifting 1-bit left or right.

## Slide 23: Datapath Operation
MOV R3, #42 // register R3 contains 42
MOV R5,#13 // register R5 contains 13
ADD R2,R5,R3 // R2 gets 42 + 13 = 55
MOV R7,R3 // register R7 contains 42

## Slide 24
3
1
1
42
Suppose we want to load the
actual value “42” into Register 3.
We can do this in one cycle!
Call this “MOV R3, #42”

## Slide 25
5
1
1
13
Suppose we want to load the
actual value “13” into Register 5.
(i.e., “MOV R5, #13”)

## Slide 26
3
1
42
Suppose we want to add the value in
R3 to the value in R5, and store the
result in R2 (“ADD R2, R5, R3”)
Cycle 1: readnum=3, loadb=1
Value in Register 3 is stored in B

## Slide 27
5
1
13
Suppose we want to add the value in
R3 to the value in R5, and store the
result in R2 (“ADD R2, R5, R3”)
Cycle 1: readnum=3, loadb=1
Value in Register 3 is stored in B
Cycle 2: readnum=5, loada=1
Value in Register 5 is stored in A

## Slide 28
0
2’b00
0
2’b00
1
13
42
55
Suppose we want to add the value in
R3 to the value in R5, and store the
result in R2 (“ADD R2, R5, R3”)
Cycle 1: readnum=3, loadb=1
Value in Register 3 is stored in B
Cycle 3: shift=00, asel=0, bsel=0
ALUop=00, loadc=1
Sum of R3 and R5 loaded in C.
Cycle 2: readnum=5, loada=1
Value in Register 5 is stored in A

## Slide 29
55
2
1
0
Cycle 1: readnum=3, loadb=1
Value in Register 3 is stored in B
Cycle 3: shift=00, asel=0, bsel=0
ALUop=00, loadc=1
Sum of R3 and R5 loaded in C.
Cycle 2: readnum=5, loada=1
Value in Register 5 is stored in A
Cycle 4: writenum=2, write=1,
Vsel=0; Sum of R3 and R5 written to R2.
Suppose we want to add the value in
R3 to the value in R5, and store the
result in R2 (“ADD R2, R5, R3”)

## Slide 30
Suppose we want to copy the contents
of R3 to R7 (“MOV R7, R3”)
3
1
42
Cycle 1: readnum=3, loadb=1
Value in Register 3 is stored in B

## Slide 31
Suppose we want to copy the contents
of R3 to R7 (“MOV R7, R3”)
Cycle 1: readnum=3, loadb=1
Value in Register 3 is stored in B
Cycle 2: shift=00, asel=1, bsel=0
ALUop=00, loadc=1,status=1
Sum of 0 and R3 loaded in C.
1
2’b00
0
2’b00
1
42
42
0

## Slide 32
Suppose we want to copy the contents
of R3 to R7 (“MOV R7, R3”)
Cycle 1: readnum=3, loadb=1
Value in Register 3 is stored in B
Cycle 2: shift=00, asel=1, bsel=0
ALUop=00, loadc=1,status=1
Sum of 0 and R3 loaded in C.
42
7
1
0
Cycle 3: writenum=2, write=1,
Vsel=0; Sum of R3 and R5 written to R2.